## Slide 1
Materials and Devices for Neural Systems and Interfaces
Sumedha Gandharava, Sepideh Rastegar, Catherine Walker, Justin Stadlbauer, Kurtis D. Cantley
Department of Electrical and Computer Engineering, Boise State University
Overview
Resistive Memory
Thin-Film Transistors (TFTs)
f
TFT Memories
Flexible Electronics
Neural Interfaces
Culturing SH-SY5Y human neuroblastoma cells on graphene-based micro electrode arrays (MEAs)
Electrical characteristics of cells are accessed via patch clamp electrophysiology
Support and Funding
Force Office of Scientific Research (AFOSR) Young Investigator Program (YIP), grant FA9550-14-1-0188.
Institutional Development Awards (IDeA) from the National Institute of General Medical Sciences of the National Institutes of Health under Grants #P20GM103408 and P20GM109095.
Boise State Department of Electrical and Computer Engineering.
Two-terminal devices that change resistance based on past current flow (Memristors)
Devices utilizing PECVD nano-crystalline silicon deposited at 250 °C or less
Ambipolar operation for complementary circuits
Use nanoparticles to trap charge over millisecond time scales
Used for artificial neural circuits with biologically realistic synaptic learning
Integration of specialized materials and devices onto mechanically flexible substrates
Piezoelectric sensors from PVDF-TrFE copolymer
(a)
[111] peak
[200] peak
[311] peak
Materials
PECVD Nano-crystalline silicon (nc-Si)
Devices
Thin-film transistors for analog, digital, and memory
Circuits
Adaptable artificial neural networks with learning and pattern recognition
Testing
Advanced electrical testing
High-k metal oxides
Metal nanoparticles
Flexible polymers
Memristors
Microelectrode arrays
Digital logic on flexible substrates
Wafer probing
Custom high-performance neural network characterization
Fig. 3 Cross-section and 3-D view of a TFT(Top left and right). Drain current versus gate voltage of a TFT(Bottom left). Input current, voltage of the input capacitor, output voltage and spike frequency of a TFT(Bottom right).
Fig. 4 Neuron Circuit fabricated using optical lithography
Fig. 7 a) Illustration of neuron cells on active microelectrode sensor arrays. b) Contact pads using Au for graphene arrays. c) Illustration of hexagonal planar graphene structure.
Fig. 8 Probe station constructed (Left), electrophysiology experiment with reservoir-mounted graphene MEA using
SH-SY5Y (human neuroblastoma line) cell (Right and below)
Fig. 5 a) AFM of CVD graphene. b) AFM of Au nanoparticles on graphene and on SiO2
Fig. 1 Plasma Enhanced Chemical Vapor Deposited (PECVD) nc-Si X-ray diffraction
(b)
(a)
(b)
(c)
Fig. 6 a), b), and c) Polymer substrates such as PET, PEN, or polyimide can be bonded to a rigid Si carrier wafer using silicon (PDMS) for simplified processing
Nanoparticle memory TFT controls short-term learning
Memristors provide long-term storage of synaptic weights
(g)
(f)
(d)
(e)
(c)
(a)
(b)
Fig. 2
Memristor cross-sections
(a) Metal-Metal contact (b) HfTiO active Layer (c) Metal-Semiconductor contact a-Si based Memristors
(d) Finalized die (e) Vias on die using photolithography method. (f) I-V characteristic of a 2umx2um device
(g) I-V characteristic of a 50umx50um device